## Slide 1
This work is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License. This presentation is released under Creative Commons-A6ribute,on 4.0 License. You are free to use, distribute and modify it ,
including for commercial purposes, provided you acknowledge the source.

## Slide 2: Module 4: Memory Management
Topic – Memory Concept
CS-2013 (Operating System)
Part V
Lecture -24

## Slide 3: Topic to be Cover
Introduction and Background of Memory Management
Memory Partitioning
Single Relocatable Partitions.
Multiple Partitions.
Multiple Fixed Partitions(MFP).
Multiple Variable Partitions(MVP).
Swapping
Contiguous Allocation
Paging
Segmentation
Segmentation with Paging.
Numerical examples.
Single Absolute Partitions.
Best-Fit,
First-Fit,
Worst Fit,

## Slide 4: Implementation of Page Table
Each operating system has its own methods for storing page tables.
  Most allocate a page table for each process.
  A pointer to the page table is stored with the other register values (like the instruction counter) in the process control block.
  When the dispatcher is told to start a process, it must reload the user registers and define the correct hardware page-table values from the stored user page table.

## Slide 5: Implementation of Page Table (Hardware Implementation of Page Table)
The hardware support for the page table can be done in many ways.
Using the set of dedicated registers.
  built with very high-speed logic
  CPU dispatcher reloads these registers.
  Instructions to load or modify the page-table registers are, of course, privileged, so only operating system can change these registers.
  This approach is satisfactory if the page table is reasonably small (not feasible).
Using Main Memory.
  Page table is kept in main memory.
  Page-table base register (PTBR) points to the page table.
  Page-table length register (PRLR) indicates size of the page table.
  In this scheme every data/instruction access requires two memory accesses. One for the page table and one for the data/instruction.

## Slide 6: Implementation of Page Table (Hardware Implementation of Page Table)
3. Translation look-aside Buffers (TLBs) ( Associative Registers)
  A special, small, fast lookup hardware cache Memory.
  It is associative, high-speed memory.
  Each entry in the TLB consists of two parts:
    A key (or tag)
    A value.
  When TLB has an item, the item is compared with all keys simultaneously.
    If the item is found, the corresponding value field is returned.
  The search is fast but hardware is expensive.
  The number of entries in a TLB is small (between 64 and 1,024).

## Slide 7: Implementation of Page Table (Hardware Implementation of Page Table)
3. Translation look-aside Buffers (TLBs) ( Associative Registers)
  it contains only a few of the page-table entries.
  When CPU generates logical address, its page number is presented to the TLB.
    If the entry is found (TLB Hit)
      its frame number is can be accessed and is used to access memory.
    If the page number is not in the TLB (TLB Miss).
      A memory reference to the page table must be made.
        When the frame number is obtained, we can use it to access memory.
        Add the page number and frame number to the TLB.
    If the TLB is already full of entries
      operating system must select one for replacement. ( LRU )
  Some TLBs allow entries to be wired down.
    TLB entries for kernel code are wired down.

## Slide 8: Paging Hardware With TLB

## Slide 9: Implementation of Page Table (Hardware Implementation of Page Table)
3. Translation look-aside Buffers (TLBs) ( Associative Registers)
  Hit Ratio : The percentage of times that a particular page number is found in the TLB.
  Example : Hit ratio = 80% .
    20 ns to search the TLB.
    100 ns to access memory.
    When Hit (120 ns)
    When Miss (20 +100 +100 =220 ns)
    To find the effective memory-access time.
    effective access time = 0.80 x 120 + 0.20 x 220 = 140 ns.
  Example : Hit ration 98%
    effective access time = 0.98 x 120 + 0.02 x 220 = 122 ns.

## Slide 10: Implementation of Page Table (Memory Protection)
Memory protection implemented by associating protection bit with each frame.
Valid-invalid bit attached to each entry in the page table:
  “valid” indicates that the associated page is in the process’ logical address space, and is thus a legal page.
  “invalid” indicates that the page is not in the process’ logical address space.

## Slide 11: Implementation of Page Table (Memory Protection)
Valid (v) or Invalid (i) Bit In A Page Table

## Slide 12: Page Table Structure
Hierarchical Paging
Hashed Page Tables
Inverted Page Tables

## Slide 13: Hierarchical Page Tables
Break up the logical address space into multiple page tables.
A simple technique is a two-level page table.

## Slide 14: Two-Level Paging Example
A logical address (on 32-bit machine with 4K page size) is divided into:
  a page number consisting of 20 bits.
  a page offset consisting of 12 bits.
Since the page table is paged, the page number is further divided into:
  a 10-bit page number.
  a 10-bit page offset.
Thus, a logical address is as follows: where pi is an index into the outer page table, and p2 is the displacement within the page of the outer page table.
page number
page offset
pi
p2
d
10
10
12

## Slide 15: Two-Level Page-Table Scheme

## Slide 16: Address-Translation Scheme
Address-translation scheme for a two-level 32-bit paging architecture

## Slide 17: Hashed Page Tables
Common in address spaces > 32 bits.
The virtual page number is hashed into a page table. This page table contains a chain of elements hashing to the same location.
Virtual page numbers are compared in this chain searching for a match. If a match is found, the corresponding physical frame is extracted.

## Slide 18: Hashed Page Table

## Slide 19: Inverted Page Table
One entry for each real page of memory.
Entry consists of the virtual address of the page stored in that real memory location, with information about the process that owns that page.
Decreases memory needed to store each page table, but increases time needed to search the table when a page reference occurs.
Use hash table to limit the search to one — or at most a few — page-table entries.

## Slide 20: Inverted Page Table Architecture

## Slide 21: Shared Pages
Shared code
  One copy of read-only (reentrant) code shared among processes (i.e., text editors, compilers, window systems).
  Shared code must appear in same location in the logical address space of all processes.
Private code and data
  Each process keeps a separate copy of the code and data.
  The pages for the private code and data can appear anywhere in the logical address space.

## Slide 22: Shared Pages Example

## Slide 23: Segmentation
Memory-management scheme that supports user view of memory.
A program is a collection of segments. A segment is a logical unit such as:
main program,
procedure,
function,
method,
object,
local variables, global variables,
common block,
stack,
symbol table, arrays

## Slide 24: User’s View of a Program

## Slide 25: Logical View of Segmentation
1
3
2
4
1
4
2
3
user space
physical memory space

## Slide 26: Segmentation Architecture
Logical address consists of a two tuple:
<segment-number, offset>,
Segment table – maps two-dimensional physical addresses; each table entry has:
  base – contains the starting physical address where the segments reside in memory.
  limit – specifies the length of the segment.
Segment-table base register (STBR) points to the segment table’s location in memory.
Segment-table length register (STLR) indicates number of segments used by a program;
segment number s is legal if s < STLR.

## Slide 27: Segmentation Architecture (Cont.)
Relocation.
  dynamic
  by segment table
Sharing.
  shared segments
  same segment number
Allocation.
  first fit/best fit
  external fragmentation

## Slide 28: Segmentation Architecture (Cont.)
Protection. With each entry in segment table associate:
  validation bit = 0  illegal segment
  read/write/execute privileges
Protection bits associated with segments; code sharing occurs at segment level.
Since segments vary in length, memory allocation is a dynamic storage-allocation problem.
A segmentation example is shown in the following diagram

## Slide 29: Segmentation Hardware

## Slide 30: Example of Segmentation

## Slide 31: Sharing of Segments

## Slide 32: Segmentation with Paging – MULTICS
The MULTICS system solved problems of external fragmentation and lengthy search times by paging the segments.
Solution differs from pure segmentation in that the segment-table entry contains not the base address of the segment, but rather the base address of a page table for this segment.

## Slide 33: MULTICS Address Translation Scheme

## Slide 34: Segmentation with Paging
Segmentation and paging can be combined to provide
  Efficiency of paging scheme
  Protection and sharing capability of the of segmentation
with simple segmentation the logical address space contains- segment Number and offset.
When paging is added the segment offset is further divided into page number and page offset.
The segment table entry contains the address of the segment’s page table.
The hardware adds the logical address’s page number bits to the page table address to locate the page table entry.
The final physical address is formed by appending the page offset to the page frame number, specified in the page table entry.

## Slide 35: Segmentation with Paging
S | P | D
Segment Table Address
+
Segment Table
+
Pf | D
Page Table
Logical Address
Physical Address
Pf

## Slide 36: Numericals
Question 1 : Why the page sizes always power of 2 ?
Answer :
All addresses are binary and are divided into page or, page frame and offset. By making the page size a power of 2, the page number, page frame number and the offset can be determined by looking at particular bits in the address; no mathematical calculation is required.

## Slide 37
Question 2:
On a simple paging scheme with following parameters:
physical memory - 224 bytes.
No of pages in logical address space - 256 pages.
page size - 210 bytes.
How many bits are in the logical address space.
Answer:
to find out the total bits in logical address space, we need to find out the total logical address space.
Total Logical address space is = No of pages*size of each page.
= 256 x 210
= 28 x 210
= 218
so an 18 bit address is required to cover 218 bytes address space

## Slide 38
Question 3:
On a simple paging scheme with following parameters:
physical memory - 224 bytes.
No of pages in logical address space - 256 pages.
page size - 210 bytes.
How many bits in the logical address space used for the page number and offset.
Answer:
total logical address space - 218 bytes ( 2M )
Size of the one page is - 210 bytes ( 2N )
so the no of bits for Page number = (M-N) bits
= 18-10
= 8 bits(no of pages)
so the no of bits for offset = N bits
10 bits

## Slide 39
Question 4 :
On a simple paging scheme with following parameters:
physical memory - 224 bytes.
No of pages in logical address space - 256 pages.
page size - 210 bytes.
How many bytes are in the page frame..
Answer:
the page frame size is same as the page size. Since page size is 210 so the frame size is also 210

## Slide 40
Question 5 :
On a simple paging scheme with following parameters:
physical memory - 224 bytes.
No of pages in logical address space - 256 pages.
page size - 210 bytes.
How many bits in the physical address is specify the page frame.
Answer:
24 bit address is required to cover 224 – bytes physical address.
page size and the frame size is same so last 10 bits out of 24 of the physical address is used as offset bits.
Remaining 14 bits specifies the page frame number.

## Slide 41
Question 6 :
On a simple paging scheme with following parameters:
physical memory - 224 bytes.
No of pages in logical address space - 256 pages.
page size - 210 bytes.
How many entries are in the page table?
Answer:
since there are 256 pages in the logical address space. So the page table must be 256 entries long.

## Slide 42: When page table parameters given….
Question 7 :
On a simple paging scheme with following parameters:
page Table entries - 512 entries.
length of page table entry -16 bits(including valid/invalid bit).
page size - 1024 bytes.
How many bits in the logical address specifies the page number and offset and how many bits are in the logical address?
Answer:
we know that total number of pages are - 512 pages
so we need to refer 512 pages - 29
so we need 9 bits to specify the page number.
offset bits = size of the page
= 1024 Bytes
= 210
So 10 bits are used to specify the offset.
so total bits in the logical address is 19.

## Slide 43
Question 8 :
On a simple paging scheme with following parameters:
page Table entries - 512 entries.
length of page table entry -16 bits(including valid/invalid bit).
page size - 1024 bytes.
what is the size of the logical address space.?
Answer:
9 bits to specify the page number.
10 bits are used to specify the offset.
bits in the logical address is 19.
so the total logical address space= 219 bytes.

## Slide 44
Question 9 :
On a simple paging scheme with following parameters:
page Table entries - 512 entries.
length of page table entry -16 bits(including valid/invalid bit).
page size - 1024 bytes.
how many bits in the physical address specify the page frame numbers and offset and also find out the total physical address space?
Answer:
  each entry in the page table is 16 bit long( including the 1 bit valid/ invalid bit. So 15 bit is the physical address is used to specify the frame number.
  offset is same in the logical address and physical address so number of bits in the physical address specifies the offset is 10.
  Total number of bits in the physical address-15+10=25 bits.
  Total physical address space is = 225 bytes.

## Slide 46
Unsolved Questions
What are the two major difference between segmentation and paging?
2. Clearly distinguish between the physical address space and logical address space of a process?
3. What is the effect of allowing two entries in a page table to point to the same frame in the memory?
4. On simple paged system, can the logical address space be larger than the physical address space?
5. Why paging is faster than segmentation?
6. Explain the difference between internal and external fragmentation.
7. What is the advantages of combining the segmentation and paging scheme into one scheme?
8. What do you understand by dynamic linking and dynamic loading.?